02		DEPARTMENT OF PROFESSIONAL AND FINANCIAL REGULATION

174		BOARD OF BOILERS AND PRESSURE VESSELS

Chapter 21:	DUTIES AND RESPONSIBILITIES OF ALL OWNERS OF BOILERS AND PRESSURE VESSELS

Summary: This Chapter establishes general duties of all owners of boilers and pressure vessels. Duties and responsibilities of owners of boilers and pressure vessels are also set forth in Title 32, Chapter 131, and elsewhere in this Chapter.

# 1.	Application for Inspection Certificates

A.	Initial Inspection. The owner of a boiler or pressure vessel must ensure that an initial inspection is conducted on a newly installed or relocated boiler or pressure vessel in accordance with the applicable provisions of Chapters 12-14 of these rules.

B.	Annual Inspection of Boilers. The owner of a boiler must ensure that the boiler is inspected annually and that the inspection is completed before the expiration of the current inspection certificate.

C.	Triennial Inspection of Pressure Vessels. The owner of a pressure vessel must ensure that the pressure vessel is inspected every 3 years and that the inspection is completed before the expiration of the current inspection certificate.

D.	Submission. The owner must ensure that the boiler or pressure vessel is inspected in sufficient time to permit compliance with this Section. The Board may assess a late inspection certificate fee against the owner if the inspection report is not submitted to the Board within 60 days after the date the current inspection certificate expires. The Board also may assess a late certificate fee if the owner fails to submit the certificate fee within 60 days of notification from the Board that the certificate fee is due.

E.	Rejection of Reports. The Chief Inspector may reject any inspection report that is incomplete or illegible or that otherwise fails to comply with the requirements of 32 M.R.S.A., Chapter 131, or the Board’s rules. If the Chief Inspector rejects the report, he must return it and a statement of the reasons for rejection to the owner and/or the Inspector.

# 2.	Expiration of Inspection Certificates

A.	Date of Expiration

(1)	Boilers. Annual inspection certificates for boilers expire on the last day of the month when the unit was last inspected and expire annually thereafter on the last day of that month unless the owner petitions the Chief Inspector to change the month of inspection on a form provided by the Board.

(2)	Pressure Vessels. Triennial inspection certificates for pressure vessels expire on the last day of the month when the unit was last inspected and expire every three years thereafter on the last day of the month unless the owner petitions the Chief Inspector to change the month of inspection on a form provided by the Board.

B.	Suspension of Operation. If an inspection report has not been submitted to the Board within 60 days of the expiration of the most recent inspection certificate, or if the owner has not paid the inspection certificate fee within 60 days after receiving notification that the inspection report has been received by the Board, or if repairs to a boiler or pressure vessel are not made within the time prescribed by the Board or the Chief Inspector, the owner must suspend operation of the boiler or pressure vessel until the Board issues a new inspection certificate.

# 3.	Orders of Correction

When the Chief Inspector issues an order of correction to an owner stating that a boiler or pressure vessel requires repair, the owner must submit satisfactory written evidence that the repairs have been completed by the time specified. The Chief Inspector must not issue a new inspection certificate for a boiler or pressure vessel that requires repair.

# 4.	Change of Status

A.	Owner. An owner must report to the Board any change in the owner’s address or telephone number within 30 days of the change.

B.	Boiler or Pressure Vessel. An owner must report to the Board any change of status with respect to a boiler or pressure vessel within 30 days of the change. As used in this Section, “change of status” means transfer of ownership, relocation, physical removal, or placement out of service.

# 5.	Accidents

A.	Reporting of Accidents

(1)	Initial Report. No later than 24 hours after a reportable accident occurs, the owner of the boiler or pressure vessel must notify the Chief Inspector and, if applicable, the insurance company. The report must include: (i) the owner’s name; (2) the location of the accident; (iii) a brief statement of facts surrounding the accident; (iv) and the name and telephone number(s) of the person(s) to be contacted regarding the accident.

(2)	Additional Information. After making the initial report required by Subparagraph (1), the owner of a boiler or pressure vessel involved in a Reportable Accident must provide to the Chief Inspector any additional information requested by the Chief Inspector regarding the accident or the boiler or pressure vessel.

B.	Maintenance of Accident Site. When a Reportable Accident occurs, no parts or appurtenances may be removed or their position changed unless necessary for the protection of life, limb, or property until the Chief Inspector has conducted his/her investigation.

C.	Suspension of Operation. When a reportable accident occurs, the owner must immediately suspend operation of the boiler or pressure vessel, and the boiler or pressure vessel must remain out of operation until the Chief Inspector has approved resumption of operation.

D.	Examination and Determination.

(1)	Examination. When a Reportable Accident occurs that results in significant injury to a person or substantial damage to equipment and/or property, the Chief Inspector must examine the boiler or pressure vessel and the circumstances surrounding the accident. The Chief Inspector may designate one or more individuals to assist in the examination.

When a Reportable Accident occurs that involves equipment failure of a boiler or pressure vessel and does not result in significant injury to a person or substantial damage to equipment, the Chief Inspector may authorize an Inspector or other individual(s) to examine the boiler or pressure vessel and to report to the Chief Inspector the findings from the examination.

(2)	Determination. After the Chief Inspector has examined, or has caused to be examined, the boiler or pressure vessel and the circumstances surrounding the reportable accident, the Chief Inspector must:

(a)	Approve the resumption of operation;

(b)	Direct that the owner suspend operation until required repairs have been made;

(c)	Summarily revoke the inspection certificate in accordance with 32 M.R.S.A. § 15119(2); or

(d)	Take other action that the Chief Inspector deems appropriate to ensure the safety of the public.

# 6.	Unsafe Conditions

If an owner becomes aware of an unsafe condition involving a boiler or pressure vessel, the owner immediately must notify the Chief Inspector in accordance with the procedure for reporting accidents specified in Section 5 of this Chapter.

# 7.	Placing a Boiler or Pressure Vessel Out of Service

A.	Boiler. When an owner voluntarily places a boiler out of service, is required to place a boiler out of service in accordance with Title 32, Chapter 131, or the Board’s rules, or is directed by the Board or the Chief Inspector to place a boiler out of service, the owner must:

(1)	Disconnect the fuel supply, if applicable; and

(2)	Disconnect the electrical power to the unit.

The owner must ensure that the work required by Subparagraphs (1) and (2) is done under the supervision of the engineer-in-charge for a power boiler, or by a technician appropriately licensed with the Oil and Solid Fuel Board or the Propane and Natural Gas Board for a low pressure boiler.

B.	Pressure Vessel. When an owner voluntarily places a pressure vessel out of service, is required to place a pressure vessel out of service in accordance with Title 32, Chapter 131, or the Board’s rules, or is directed by the Board or the Chief Inspector to place a pressure vessel out of service, the owner must:

(1)	Disconnect the source of pressure input; and

(2)	Remove the relief valve.

The owner must ensure that the work required by subparagraphs (1) and (2) is done by an individual who is familiar with the hazards associated with the particular pressure vessel.

8.	Personnel for Power Boilers

A.	The owner of a plant operating a power boiler must designate a person to be the engineer-in-charge of the plant. The designated person must have an appropriate license for the plant based on the classes of licensure specified in 32 M.R.S.A. § 15109.

B.	The owner of a power boiler must, at the time of installation and upon any change in the identity of the engineer-in-charge, inform the Board in writing of:

(1)	The name(s) and address(s) of any person(s) designated engineer(s)-in-charge;

(2)	The date when each person designated engineer-in-charge assumed that position; and

(3)	The precise location and the registration number(s) of the power boiler(s) each engineer-in-charge will oversee.

9.	Heating Boilers

The owner must ensure that heating boilers are properly maintained by appropriately licensed individuals to ensure safe and reliable operation at all times.

10.	Personnel for Pressure Vessels

A.	Regardless of the number of pressure vessels installed at a plant, the owner remains responsible for ensuring that the pressure vessels are maintained and operated in a safe condition.

B.	Whenever 10 or more pressure vessels are installed at a plant, the following requirements apply:

(1)	The owner must assign an individual who is responsible for ensuring that the pressure vessels are maintained and operated in a safe condition as required by these rules; and

(2)	Duties relating to the operation and maintenance of the pressure vessels must be performed under the direct authority of the individual assigned responsibility in accordance with paragraph A.

11.	Tests

An Inspector may at any time require an accumulation test or other test to determine if a boiler or pressure vessel is operating properly.

# 12.	Inspection Certificate

A.	Subject to the provisions of 32 M.R.S.A. § 15121(1) and (2), an owner may not operate a boiler or pressure vessel without a current, valid inspection certificate. The Board must issue inspection certificates for boilers for a period of 12 months and for pressure vessels for a period of 36 months.

# B.	An owner may obtain an inspection certificate from the Board if the following requirements have been satisfied:

(1)	An Inspector has inspected the boiler or pressure vessel and has submitted the report of inspection to the Board;

(2)	The Chief Inspector has approved the inspection report; and

(3)	The Board has received payment for the inspection certificate, or for the inspection if performed by the Chief Inspector or the Deputy Inspector.

C.	In order to coordinate Inspectors’ availability with the operating needs of the facility, the Chief Inspector may authorize an extension of up to 2 months beyond the expiration date of the inspection certificate. Except in cases of emergency, a written request to operate the boiler or pressure vessel beyond the expiration date must be submitted to the Chief Inspector no less than 15 days before the expiration date.

# 13.	Boilers or Pressure Vessels Found to be Unsafe

A.	Suspension of Inspection Certificate. If an Inspector finds that a boiler or pressure vessel is unsafe to operate, the Inspector must notify the Chief Inspector immediately. The Chief Inspector must suspend the inspection certificate, and the owner must immediately suspend operation of the boiler or pressure vessel until the Chief Inspector approves the placing of the boiler or pressure vessel back in operation. Pursuant to 5 M.R.S.A. §10004(4), a suspension issued in accordance with this paragraph is effective for a period of not more than 30 days.

B.	Condemnation and Stamping. In the event that repairs to a boiler or pressure vessel are not feasible, the Chief Inspector must revoke the certificate and condemn the boiler or pressure vessel. Upon condemnation, the Chief Inspector must stamp the boiler or pressure vessel (“XXX Me”) in accordance with 32 M.R.S.A. § 15112, provided that the actual stamping must be stayed during the 7-day period set forth in Section 13, paragraph C of this Chapter and during the pendency of any appeal filed with the Board. Only the Chief Inspector may revoke a certificate and condemn a boiler or pressure vessel. Pursuant to 5 M.R.S.A. § 10004(4), a revocation issued in accordance with this paragraph is effective for a period of not more than 30 days.

# C.	Owner’s Right to Appeal. When the Chief Inspector suspends or revokes a certificate, the Chief Inspector must give the owner written notice of the owner’s right to appeal the suspension or revocation to the Board within 7 calendar days of the suspension or revocation.

# D.	Appeal Hearing. Upon receipt of a timely appeal from the owner, the Board will schedule an appeal hearing pursuant to 32 M.R.S.A. § 15104-A(2). The provisions of the Maine Administrative Procedure Act relating to adjudicatory proceedings govern the hearing. The Chief Inspector bears the burden of proof at the appeal hearing. The boiler or pressure vessel that is the subject of the appeal must remain out of service and may not be operated during the pendency of the appeal.

14.	Portable Boilers

Whenever a portable boiler is installed for temporary use, an external inspection must be completed within 72 hours, provided the portable boiler has a current, valid inspection certificate issued by the State of Maine. If the portable boiler does not have a current, valid inspection certificate, a certificate inspection is required prior to operation. The owner of the boiler shall arrange for the required inspections to be conducted.

Note: It is recommended that the owner of portable boilers which may be rented out to facilities located in the State of Maine have the boilers inspected by an Authorized Inspector licensed by the State of Maine as required so the boilers have a current valid certificate on a continuous basis. This will expedite the installation of a portable boiler and reduce the likelihood of the boiler being shutdown to complete the internal inspection prior to continued operation at a site.

15.	General Responsibility

Owners must ensure that all boilers, pressure vessels, and appurtenances are operated, inspected, and maintained in a condition sufficient to safely perform the work for which they were intended and are kept sufficiently clean to prevent fire hazards.

# AUTHORITY: 	32 M.R.S.A. § 15104-A, § 15119, and § 15121

# EFFECTIVE DATE:

# January 15, 2005 – filing 2005-29